FT-90 - 50w vhf/35w uhf, 180 ch, 2 home ch, CTCSS/DCS, 100-230, 300-530, 810-999 MHz, 13.8vDC, 9.5A tx

FUNCTION				SINGLE PRESS			LONG PRESS

Set button - (programmable)		in memory mode alpha or freq	enter/exit menus								in vfo mode changes vhf/uhf

Left button - (programmable)		VFO/Memory mode			prog channel

Right Button - (programmable)	repeater shift, auto, +, -, simplex

DISP button - bottom line of display	DC voltage/control/key function	Smart Search

DIAL - press and rotate to 		select MHz in VFO mode		mem to VFO

Microphone buttons

Direct keypad entry of frequency 	1,4,6,9,4,0 = 146.940    4,3,3,# = 433.000

Up or Down buttons			changes one channel up or down	Hold to start scan

lock - locks mic buttons

ACC-  now programmed for priority	select priority scan on/off (ch. #1)

VFO/MR				change between memory/VFO	hold to program

P1 - now programmed for		home channel select function

P2 - now programmed for		power level select

Lamp - turns on keypad backlight

Press SET in scan mode to temporary skip busy channel until scan is started again

STORE MEMORY - select VFO mode with VFO/MR, SET to change VHF/UHF,  select frequency w/ DIAL, (press DIAL for 1 mHz), set shift, CTCSS, power level using menus - press VFO/MR for 1 sec, display flashes, select memory channel, press VFO/MR again to store. (if freq shows then there is something already stored there.)

SELECT MEMORY ch. VFO/MR to MEM, rotate DIAL or press up down buttons on mic to change channels.

COPY MEMORY ch to VFO - select memory ch, press DIAL for 1 sec to copy to VFO, radio switches to VFO

ERASE MEMORY - on mem channel, press VFO/MR for 1 sec, press DISP, mem is erased and ch 1 is displayed

MEMORY ONLY MODE - turn on radio while pressing VFO/MR, VFO mode cannot be entered, repeat for normal

PRIORITY -  select VFO or MEM ch other than #1, press ACC key to start pri scan, not in scan mode, PTT to stop

CPU RESET - SET and DISP while turning power on.

MASTER RESET - right and left arrow keys plus DISP while turning power on, erases all memory and menu sets

MENU FUNCTIONS

1 	alpha tag on/off			20	front panel key lock on/off

2	store alpha tags			21	set packet baud rate

3	APO set				22	program left arrow key

4	not used				23	program right arrow key

5	ARTS mode				24	program mic P1 key

6	key beep on/off			25	program mic P2 key

7	CW id on/off				26	program mic ACC key

8	CW id programming			27	adj RF squelch min level

9	display contrast			28	set rptr shift direction

10	display illumination			29	set scan resume mode

11	DC input voltage			30	set rptr shift magnatude

12	set DCS code				31	on/off skip during scan

13	DCS search				32	set freq steps 5,10,12.5,15,20,25,50 kc

15	DTMF autodial delay time		33	set CTCSS/DCS mode

14	DCS normal/invert			34	set tone frequency

16	DTMF sending speed			35	set time out timer

17	program autodialer			36	1/2 deviation - 2.5kc

18	set fan mode				37	TX power level  5,10,20,50

19	PTT lock on/off			38	AM/FM receive mode